Manual for T 6x6 and T4x4
- Online manual : https://www.3dtlac.xyz/navody/
  A few words about the building .....
- read the whole manual before construction
- I leave the material to the customer's choice.
- I've found that if I recommend PETG, for example, not everyone can print it out nicely. ABS does not hold on another bed.
- The model is designed so that if you choose your favorite material it will print without any problems. I have already printed them from PETG, ABS, PLA, CPE.
- Choose a material best for your printer and has beautiful layers.
- I recommend a layer of 0.2 mm, just 20% fill. For bearings use and caradans use min 75% infill.
- For tires 5%
- But if your printers combine layers, take advantage of it. Alternatively, if you want a very detailed surface, print on a 0.1 mm layer.

---
You will need:
- bearings 10x15x4 – 28 pcs
- screws M3 x 10 mm - 150 pcs
- screws M3 x 14 mm - 40pcs
- screws M3 x 16 mm – 20pcs
- screws M2 x 10 mm – 60pcs
- locking screws M3 x 6 mm (coils) - 50pcs
- nuts M2 – 60 pc
- nuts M3 - 50pcs
- screws M6 x 55 mm - 2pcs
- screws M6 x 100 mm - 4 pcs
- screws M6 x 30 mm - 10pcs
- nuts M6 - 20 pcs (necessary glue - or you can try lock nuts)
- threaded rod dia 3mm and 190-195mm long 2x
- Screws M4 x 40mm – 2x

---
Step 1

---
Step 2

---
Step 3

---
Step 4

---
Step 5

---
Step 6

---
Step 7

---
Step 8

---
Step 9

---
Step 10

---
Step 10/2

---
Step 11

---
Step 12

---
Step 13

---
Step 14

---
Step 15

---
Step 16

---
Step 17
In this step, the T 6x6 version continues, for the T 4x4 Trial version go to the end of the manual.

---
Step 18

---
Step 19

---
Step 20

---
Step 21
this step is for suspension version A
if you want use suspension version B dont use MOTOR part and motor gearbox – use big gearbox

---
Step 21 – big gearbox

---
Gearbox motor – dont use if you use big gearbox

---
Gearbox motor step 2
dont use if you use big gearbox

---
Step 22

---
Step 23

---
Step 24

---
Suspension A

---
Suspension B

---
Suspension B

---
Trial T 4x4 version

---
Trial T 4x4 version

---
Trial T 4x4 version

---
Trial T 4x4 version

---
Trial T 4x4 version